## Slide 1: Pompano Culture in Recirculating Aquaculture Systems
Paul S. Wills
Funding Thanks to

## Slide 2: Inland Recirculating Aquaculture Systems

## Slide 3: Recirculating Aquaculture Systems (RAS)
Year round growing season
Reduced water consumption
Reduced effluent discharge
Intensive production
Enhanced biosecurity
Increased food safety
Containment of escapees
Environmental Sustainability

## Slide 4: Basic RAS Design Waste Water Makeup Water & Evaporation
Biofiltration
Solids Filtration
Concentrated Waste Sludge
Ammonia
(Highly Toxic)
Nitrate
(very low toxicity)
Solid and Dissolved wastes
Oxygen
Feed

## Slide 5: Advanced RAS design and Operation
HBOI-FAU ACTED Workshop:
“Recirculating Aquaculture Systems: Design, Engineering and Operation”
Instructors: Michael Timmons and Jim Ebeling Dates: October 17-19, 2013
Cost: $450
Information: See Jill Sunderland or, www.aquaculture-online.org or, www.fau.edu/hboi
or, call 772-242-2506

## Slide 6: Basis of the Commercial System Design
Scaled up version of tested design developed jointly for USDA-ARS project and FL-FWCC marine hatchery program FMFEI
System Tested with:
  Red Drum up to ~90 Kg/m3
  Florida Pompano ~40 Kg/m3

## Slide 7: LOW HEAD GROWOUT SYSTEM
1. Long flow pathway moving bed reactor with cross flow oxygenator, float valves, and propeller pump; 2. Incoming salt and freshwater lines with float valves and water meters; 3. UV sterilizer; 4. Torrus filters with 13ft3 of MB3 floating plastic media; 5. Ten-foot diameter tanks w/ center sump and sidebox drain; 6. Diverter box; and 7. 60 micron drum filter.
1
2
3
4
5
6
7

## Slide 9: BIOFILTER VOLUMETRIC NITRIFICATION RATES
Long Flow Pathway Moving Bed Biofilter
150.0
125.0
100.0
75.0
50.0
25.0
0.0
175.0
0.00
0.20
0.40
1.20
1.40
1.60
0.60 0.80 1.00
Influent TAN (mg/L)
g TAN/m3 media-day

## Slide 10: Commercial System Design
Not to scale
* Static Bed filters each contain 8 ft3 of MB3 biomedia
*

## Slide 11: Panorama of Filtration System
Biofilter Drum Screen Filter
Foam Fractionator
Main Pumps
Return Water
Pumping BSatsaitnic Bed Filters Ultraviolet filters

## Slide 12: Drum Screen Filter

## Slide 13: Microscreen Cleaning Process

## Slide 14: Waste Water Recapture
We used a Static Bed Filter to separate solids from Drum Screen Filter Waste stream
  Concentrates solids prior to discharge
  Recaptures significant component of water used for wash down of drum screen
  Each contains 8 Ft3 MB3 Media

## Slide 15
14.9 + 17.4
43.2 + 12.0
10.3 + 8.5
50
45
40
35
30
25
20
15
10
5
0
Removal Efficiency (%)
Swirl separator Static bed Moving bed
-6.5 + 2.1
22.2 + 1.7
6.8 + 2.1
-10.0
5.0
0.0
-5.0
10.0
25.0
Removal Efficiency (%)
Swirl separator
20.0 Static bed
Moving bed
15.0
Solids removal efficiency
RE = (TSSIN-TSSOUT) / TSSIN
Solids removal efficiency (< 50 microns)

## Slide 16: Moving Bed Biofilter (250 ft3 MB3 Biomedia)
Aeration Keeps Bed Fluidized

## Slide 17
Minimum Dose Desired
30,000 uW sec/cm2
The two units delivering
~150,000 uW sec/cm2

## Slide 18: Tank Cover

## Slide 19: Aeration and Oxygenation

## Slide 20: Aeration and Oxygenation
Oxygenation Zone 2
Aeration Zone
Oxygenation Zone 1
O2
Sensors
25 ft Diameter

## Slide 21: Backup Systems
Systems designed to combat “Murphys Law”
  “If anything can go wrong it will”
Therefore managers must:
  Anticipate
  Plan
  Train
  Respond
    (an automatic system that “cries wolf” can derail this necessary task)

## Slide 22: Backup Systems
Generators
Automatic oxygen system

## Slide 23: Generators
Must have disconnect switch and meet other local requirements

## Slide 25: Automatic Oxygen System
Opens oxygen flow to tanks regardless of monitoring systems or other backup systems if the power turns off
Must use Normally Open Solenoid Valves for failsafe system
– Normally open  closed when power applied

## Slide 26: Broodstock Conditioning and Spawning System USDA-ARS/HBOI-FAU Design

## Slide 27: Broodstock Profile
Florida Pompano
Weight: 0.7 – 2.3 kg
Mature age: 1- 3 yrs
Temp: 18 – 30 C
Salinity: 5 – 36 ppt

## Slide 28: Water Quality Management Parameters
Parameter Temperature pH
Dissolved oxygen Alkalinity Ammonia
Nitrite
Total dissolved solids
Target Level 16 – 30 C
7.6 – 8.2
≥ 5 mg/L
≥ 200 mg/L
≤ 1 mg/L
≤ 2 mg/L
≤ 5 mg/L

## Slide 29: Broodstock Conditioning System
Waste
UV
Sump (2.3 m3)
Culture Unit (5.7 m3)
Egg Collectors (0.3 m3)
Waste
Beadfilter (0.1 m3)
Pump to chiller
Waste
Cartridge filters
Return from chiller

## Slide 32: Larviculture System

## Slide 33: Nursery System

## Slide 34: Limitations of RAS Technology
Waste products from the fish must be treated before discharge
– This is much easier than in other aquaculture systems such as open ocean net-pens
No one has ever achieved 100% recirculation due to water needed for removing waste products and lost to evaporation
WASTES !!!!!

## Slide 35: WASTES!!! WHAT?! WASTE !!!!!
What are they?
  Uneaten feed and other Solids
  Liquid Excretions
One Characteristic of these “Wastes” is that they contain quite a bit of nutrient
  (esp., Nitrogen, Phosphorus)
So, why not USE nutrients instead of discharging them?

## Slide 36: The Answer: Integrated Multi-Trophic Aquaculture (IMTA)
Turn Wastes into Resources
The Next Generation in Recirculating System Design
IMTA = Integrated Multi-trophic Aquaculture Systems

## Slide 37: Prototype Land Based HBOI-IMTA Funded Through Aquaculture SLP
Assimilative Culture
Fed Culture
Filtration Systems
Solids
Prepared Feed
Extractive Culture Settleable Solids
Fed Culture
Extractive Culture Suspended Solids
Prepared Feed